## Slide 1: Towards Content-Oriented Orchestration for Virtual Information Centric Networking
Long HOANG MAI & Guillaume DOYEN, on behalf of the Doctor consortium
Troyes University of Technology – Charles Delaunay Institute
Contact : guillaume.doyen@utt.fr
ICNRG Interim Meeting (IETF #101) – London – March 18, 2018

## Slide 2: Locks for an ICN deployment
A pragmatic approach
  A progressive migration performed according to opportunities
    Services that would benefit from an ICN stack at most
    Topological locations (access, edge, core) that best fit with ICN Traffic Engineering features (e.g. symmetric routing, caching)
  Management and security frameworks are required
  Cohabitation with IP can be handled through NFV
    Isolation of network protocol stacks (keeps IP as a common substrate)
    Cost effective solution by using commodity servers
  This is the position of the 2014-2018 Doctor Project
    Funded by the (French) National Research Agency (ANR)
    Selected NDN as a target ICN technology

## Slide 3: Content-Oriented MANO - PoC
Computing
Resources
Storage
Resources
Network
Resources
Virtualisation Layer
iGW
NFVI
eGW
router
Virtual Computing
Virtual Storage
Virtual Network
Or-Vi
Or-Vnfm
Vi-Vnfm
Ve-Vnfm-em
TOSCA
Parser
Cyber
CAPTOR
TOSCA PROCESSOR
TOSCA
Descriptors
NFD Agent
MMT Probe
NFD Agent
MMT Probe
NFD Agent
MMT Probe
NFV Instances
NFVI Resources
VNF
Catalogue
NS
Catalogue
Orchestrator engine
EM
EM
EM
VNF
Manager
NFV Orchestrator
vnf-em
Infrastructure Controller
Nf-vi
Tenant Network Controller
Virtualised
Infrastructure
Manager
MMT
Operator

## Slide 4: Content-Oriented MANO - PoC
Management
  NDN VNF monitoring (ext. of NFD mgmt protocol)
  Design and implementation of micro-detectors [IM 2015, WIFS 2015]
  Event correlation [NOMS 2018]
  A management Dashboard (partner Montimage)
Orchestration
  A TOSCA extension
    Specifying an NDN service topology
    Specifying dynamic policies
  Implementation of a NDN orchestrator
    A chain of MANO Components processing

## Slide 5: A TOSCA extension for ICN (1)
Virtual Deployment Unit
  Abstraction describing the virtual resources over which a VNF will be executed
Virtual Network Function
  The piece of software that will be executed on a VDU
  NDN router, ingress gateway, egress gateway and NDN firewall
Virtual Link
  Resources required to link two VDUs
Connection Point
  The connection capability which associates a VDU to a virtual link
Forwarding Path and Graph
  a list of VNFs that a particular set of NDN packets will follow
  Uses content prefixes instead of L2/L3 flow specifications

## Slide 6: A TOSCA extension for ICN (1)
Policies
  Event-Condition-Action rules to apply dynamically
  Signature verification policy: change the NDN router mode (signature verification to be applied on data packets)
  The firewall policy: configure, at runtime, firewalls mode and configuration (i.e., white and black lists);
  The scaling policy: monitor VNFs performance metrics and enforce a scaling-out action when a threshold is crossed

## Slide 7: Demonstration scenario
European telco topology
  ClaraNet (6 PoP part of)
  Points of Presence (PoP) made available through the Internet Zoo Topology Dataset
Different NDN VNFs
  NDN routers
  Signature verification module
  NDN Firewall
  Ingress/egress gateways (not included)
The whole network is deployed through virtualized means
  1 PoP in 1 Openstack VM
NDN compromised server sends poisoned content
Attack mitigation through dynamic orchestration
By claranet (claranet) [CC0], via Wikimedia Commons

## Slide 8: Topology
VDU1
VDU2 – ID2
VDU6 – ID3
VDU7 – ID5 -
VDU8 – ID7
VDU9 – ID9
VDUX – ID10
VDU3 – ID4
MADRID
VDU4 – ID6
VDU5 – ID8
Lisbon POP
London POP
Berlin POP
Amsterdam POP

## Slide 9: TOSCA VNF and VDU specifications
router_2:
type: tosca.nodes.nfv.doctor.VNF
properties:
id: 2
vendor: orange
version: 1.0
requirements:
- VDU: VDU2
firewall_1:
type: tosca.nodes.nfv.doctor.VNF.firewall
properties:
id: 6
vendor: orange
version: 1.0
configuration:
mode: accept
rules:
- action: append-drop
prefix: [/foo]
requirements:
- VDU: VDU4
VDU2:
type: tosca.nodes.nfv.doctor.VDU
properties:
name: VDU2
sw_image: maouadj/ndn_router:v1
config: /doctor/launch_nfd_router.sh
flavor: medium
placement_policy: ['popLocation==uk’]
VDU4:
type: tosca.nodes.nfv.doctor.VDU
properties:
name: VDU4
sw_image: maouadj/ndn_firewall:v1
config: /doctor/launch_ndn_firewall.sh
flavor: medium
placement_policy: ['popLocation==netherlands']

## Slide 10: TOSCA VL and CP specifications
VL1:
type: tosca.nodes.nfv.doctor.VnfVirtualLinkDesc
properties:
name: VL1
connectivity_type: VXLAN
VDU1_VL1_CP:
type: tosca.nodes.nfv.doctor.Cpd
properties:
name: VDU1_VL1_CP
layer_protocol: VXLAN
requirements:
- virtual_link: VL1
- virtual_binding: VDU1

## Slide 11: TOSCA Forwarding Path Specification
http_from_r2_to_as1:
type: tosca.nodes.nfv.doctor.FP
description: creates path for /http from r2 to as1
properties:
id: 2
policy:
type: NDN
prefix: [/com/google]
path:
- forwarder: router_2
capability: VDU2_VL10_CP
- forwarder: router_x
capability: VDUX_VL10_CP
- forwarder: router_x
capability: VDUX_VL2_CP
- forwarder: router_4
capability: VDU3_VL2_CP
- forwarder: router_4
capability: VDU3_VL3_CP
- forwarder: firewall_1
capability: VDU4_VL3_CP
- forwarder: firewall_1
capability: VDU4_VL4_CP
- forwarder: peering_router_1
capability: VDU5_VL4_CP

## Slide 12: Dynamic orchestration for CPA mitigation
VDU1
VDU2 – ID2
VDU6 – ID3
VDU7 – ID5 -
VDU8 – ID7
VDU9 – ID9
VDUX – ID10
VDU3 – ID4
MADRID
VDU4 – ID6
VDU5 – ID8
Lisbon POP
London POP
Berlin POP
Amsterdam POP

## Slide 13: Content Poisoning Attack scenario
Legitimate user
  Requests content among 1 million whose popularity follows zifp law
  Average rate of 10 Interests/s following a Poisson law
Attacker consumer
  Send Interests for popular contents
  Top most 1% (10 000 contents) at the 64 Interests/s fixed rate
Network
  Setup with a multicast routing strategy
  Do not enforce signature verification for performance purposes
Attacker provider
  Pushes poisoned Data to routers
Legitimate user
  Detects invalid signatures and asks for newer version of the same content
  Competes with the attacker client

## Slide 14: TOSCA policies specifications
policies:
- CPA_countermeasure:
type: tosca.policies.nfv.doctor.security.signature_verification
targets: [router_4, router_5]
triggers:
peeringPoint1_verification:
event_type: tosca.nfv.doctor.security.alert.cpa
condition:
constraint: triggred_by router_2
action:
action_type: update_router_mode
mode: signing
target_router: router_4
Dynamically starts the signature verification enforcement if a CPA alert is raised

## Slide 15: TOSCA Policies Specification
policies:
- update_firewall:
type: tosca.policies.nfv.doctor.ndn.security.update_firewall
targets: [firewall_1, firewall_2]
triggers:
peering_point_1:
event_type: tosca.nfv.doctor.security.alert.poisoned_content
condition:
constraint: triggred_by router_4
action:
action_type: update_firewall
target_firewall: firewall_1
Dynamically updates the firewall black list with prefixes whose signature is invalid

## Slide 16: TOSCA Policies Specification
policies:
- scaling_out_policy:
type: tosca.policies.nfv.doctor.ndn.scaling
targets: [router_4, router_5]
triggers:
scale_out:
meter_name: PIT
event_type: tosca.policies.nfv.doctor.ndn.utilization
condition:
constraint: pending_interests greater_than 10
threshold: 10
comparison_operator: gt
period: 10
action:
action_type: scale_out
number: 3
Dynamically spawn NDN routers to cope with the resource exhaustion due to signature verification

## Slide 17: Outline
Context
  On the maturity of the ICN paradigm
  Locks for an ICN deployment
On the road for an ICN deployment
  Service migration
  Management and security
  Infrastructure means
Leveraging NFV as an ICN enabler
  Opportunities and challenges
  Proposition of a Network Function Virtualization Infrastructure
  ICN Management and Orchestration
Demonstration
Conclusion and perspectives

## Slide 18: Conclusion and perspectives
An ongoing work toward the design and implementation of NFV-MANO components for NFV
  A proof of concept of the whole architecture
  Code availability
    https://github.com/DOCTOR-ANR
Doctor and ICNRG
  Doctor is open to serve ICNRG efforts to push forward the deployment and standardization of this network paradigm
Future work
  Evaluate the benefits of an NDN virtual network carrying web traffic with real end-users
  Further explore the content orchestration
  Explore micro-services orchestration for NDN

## Slide 19: Questions ?

## Slide 20: References
M. Vahlenkamp, F. Schneider, D. Kutscher and J. Seedorf, "Enabling Information Centric Networking in IP Networks Using SDN," Future Networks and Services (SDN4FNS), 2013 IEEE SDN for, Trento, 2013, pp. 1-6.
S. Salsano, N. Blefari-Melazzi, A. Detti, G. Morabito, L. Veltri, "Information centric networking over SDN and OpenFlow: Architectural aspects and experiments on the OFELIA testbed", Computer Networks, Volume 57, Issue 16, 13 November 2013, Pages 3207-3221, ISSN 1389-1286
N. L. M. van Adrichem and F. A. Kuipers, "NDNFlow: Software-defined Named Data Networking," Network Softwarization (NetSoft), 2015 1st IEEE Conference on, London, 2015, pp. 1-5.
X. N. Nguyen, D. Saucez and T. Turletti, "Efficient caching in content-centric networks using OpenFlow," INFOCOM, 2013 Proceedings IEEE, Turin, 2013, pp. 1-2.
Peyman TalebiFard, Ravishankar Ravindran, Asit Chakraborti, Jianli Pan, Anu Mercian, Guoqiang Wang, Victor C.M. Leung, "An Information Centric Networking approach towards contextualized edge service," 2015 12th Annual IEEE Consumer Communications and Networking Conference (CCNC), Las Vegas, NV, 2015, pp. 250-255.
Pedro Henrique V. Guimaraes, Lyno Henrique G. Ferraz, Joao Vitor Torres, Diogo M. F. Mattos, Andres F. Murillo P., Martin E. Andreoni L., Igor D. Alvarenga, Claudia S. C. Rodrigues, Otto Carlos M. B. Duarte, “Experimenting Content-Centric Networks in the Future Internet Testbed Environment”, ICC 2013 Workshops, IEEE, 2013.
Salvatore Signorello, Radu State, Jérôme François, Olivier Festor:NDN.p4: Programming information-centric data-planes. NetSoft 2016: 384-389

## Slide 21: Related Project publications
[NOMS 2018] Hoang Long Mai, Tan Nguyen, Guillaume Doyen, Rémi Cogranne, Wissam Mallouli, Edgardo Montes de Oca, Olivier Festor. Towards a Security Monitoring Plane for Named Data Networking and its Application against Content Poisoning Attack. To appear in NOMS 2018 - 2018 IEEE/IFIP Network Operations and Management Symposium
[IM 2017] Tan N. Nguyen, Xavier Marchal, Guillaume Doyen, Thibault Cholez, Rémi Cogranne. Content Poisoning in Named Data Networking: Comprehensive characterization of real deployment. IM 2017: 72-80
[ICN 2016] Xavier Marchal, Moustapha El Aoun, Bertrand Mathieu, Wissam Mallouli, Thibault Cholez, Guillaume Doyen, Patrick Truong, Alain Ploix, Edgardo Montes de Oca. A virtualized and monitored NDN infrastructure featuring a NDN/HTTP gateway. ICN 2016: 225-226
[IM 2015] Tan N. Nguyen, Rémi Cogranne, Guillaume Doyen. An optimal statistical test for robust detection against interest flooding attacks in CCN. IM 2015: 252-260
[WIFS 2015] Tan N. Nguyen, Rémi Cogranne, Guillaume Doyen, Florent Retraint:Detection of interest flooding attacks in Named Data Networking using hypothesis testing. WIFS 2015: 1-6

## Slide 22: Outline
Context
Leveraging NFV as an ICN enabler
  Overall architecture
  NDN Monitoring and management
  NFV Orchestration
Demonstration
  Initial orchestrated deployment
  Dynamic Content Poisoning Attack mitigation
Conclusion and perspectives

## Slide 23: Outline
Context
Leveraging NFV as an ICN enabler
  Overall architecture
  NDN Monitoring and management
  NFV Orchestration
Demonstration
  Initial orchestrated deployment
  Dynamic Content Poisoning Attack mitigation
Conclusion and perspectives

## Slide 24: On the maturity of the ICN paradigm
On the design part
  One decade of research and development
  Basic topics have been covered
  Advanced subjects are on interest
On the implementation part
  Functional implementations are available
  Open testbeds are also deployed
  Device manufacturers start implementing ICN stacks
-> ICN is ready for deployment considerations

## Slide 25: NFD monitoring [NOMS 2018]
Component | Metric | Description
Faces | In Interest | Periodic number of incoming Interests
 | In Data | Periodic number of incoming Data
 | In NACK | Periodic number of incoming NACK
 | Out Interest | Periodic number of outgoing Interests
 | Out Data | Periodic number of outgoing Data
 | Out NACK | Periodic number of outgoing NACK
 | Drop Interest | Periodic number of dropped Interests
 | Drop Data | Periodic number of dropped Data
 | Drop NACK | Periodic number of dropped NACK
Content Store | CS Insert | Periodic number of Data insert in CS
 | CS Miss | Periodic number of cache miss in CS
 | CS Hit | Periodic number of cache hit in CS
Pending Interest Table | PIT Create | Periodic number of PIT entries created
 | PIT Update | Periodic number of updates in PIT
 | PIT Delete | Periodic number of PIT entries deleted
 | PIT unsatisfied | Periodic number of PIT entries unsatisfied
 | PIT Size | Periodic number of PIT entries
 | PIT Entries time | Average time in PIT for entries

## Slide 26: NDN Event Management [NOMS 2018]
Understanding NFD pipelines for anomaly detection
Correlating events

## Slide 27: NDN Orchestration
NFVO Core
  Initial deployment of a NDN service
    Deploy virtual networks
    Deploy virtual units
    Connect virtual units to virtual networks
    Retrieve VDU and networks configurations (NDN Engine)
    Make sure that VNFs are in the correct state
    Engage VNFs configuration (NDN Engine)
    Start monitoring probes and event correlators
NDN Engine
  Generates the appropriate NDN configurations for each VNF
    NDN paths and strategies + NFVI information (IP addresses, identifiers, etc.) -> FIB entries

## Slide 28: NDN Orchestration
VNF Manager
  Responsible for the life-cycle management of NDN VNF
  VNF <-> VNFM <-> NFVO
    Receives initial configurations and dynamic reconfigurations from NFVO and pushes them into VNFS
    Sends notifications (security alerts) from VNF and send them the NFVO

## Slide 29: Outline
Context
Leveraging NFV as an ICN enabler
  Overall architecture
  NDN Monitoring and management
  NFV Orchestration
Demonstration
  Initial orchestrated deployment
  Dynamic Content Poisoning Attack mitigation
Conclusion and perspectives

## Slide 30: ETSI NFV MANO
Computing
Hardware
Storage
Hardware
Network
Hardware
Hardware resources
Virtualisation Layer
Virtualised
Infrastructure
Manager(s)
VNF
Manager(s)
VNF 2
NFV
Orchestrator
OSS/BSS
NFVI
VNF 3
VNF 1
Virtual Computing
Virtual Storage
Virtual Network
NFV Management and Orchestration
EM 2
EM 3
EM 1
Service, VNF and Infrastructure Description
Or-Vi
Or-Vnfm
Vi-Vnfm
Os-Ma
Ve-Vnfm
Nf-Vi
Vn-Nf
Vl-Ha
Source : ETSI GS NFV-MAN 001